## Slide 1: CMPE110: Computer Architecture CMP
Ehsan K. Ardestani

## Slide 2: Quiz #4
  Write Down one positive and one negative property for each of these VM/Cache integration schemes
  PIPT:
  + No aliasing
  - Translation before access to cache (Performance)
  - Every access needs translation (Power/Energy)
  VIVT
  + No translation needed before access (Performance)
  + No translation needed before access (Power/Energy)
  - Aliasing
  VIPT
  + No aliasing
  + No extra cycle for translation
  - Translation needed for every access (Power/Energy)
  Which one you recommend?
  Depends on application and constraints, but in general, VIPT has more pros.

## Slide 3: Performance Basics: Latency
Latency: wall-clock time, elapsed time,…
  Medical dictionary definition:
    the interval between stimulation and response
  How long it takes to do X?

## Slide 4: Performance Basics: Throughput
Throughput or bandwidth
  Webster definition:
    the amount of material, data, etc., that enters and goes through something
  I would rather say:
    The rate that a unit of work is completed or started by a mechanism
  How much X work is done in a given time?

## Slide 5: Ways to improve performance
Faster technology (higher clock frequency)
Better compiler (lower IC)
More efficient pipelines (better CPI)
Parallelism
  Instruction-level parallelism
    Out-of-Order techniques
    Super scalar pipelines
  Parallel processing
  Job-level parallelism

## Slide 6
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Our processor, Intel Pentium 4 | SIMD: SSE instructions, multimedia extensions
 | Multiple | MISD: No example | MIMD: Intel Xeon

## Slide 7: Chip-level Multiprocessing
Multiple processor on the same chip
  Collection of processing elements that co-operate to solve a problem
  hopefully faster than one core alone
Why do we care about multiprocessing?
  Getting harder to improve performance by lowering latency
    Power and thermal issues
  Increase throughput
Issues
  communication and synchronization
    how is data shared among cores?
    how is co-operation achieved?
    Shared Memory Model, Message Passing Model
  sizing
    how large a collection of cores?
    how powerful is each core?
    how much memory?
  performance and scalability
    how does this scale?

## Slide 8: Measuring Performance
Speedup?
  measured against execution time of best available sequential code
  data set remains constant
1
1
Ideal
Well programmed
Bad programmed

## Slide 9: Measuring Performance
Efficiency?
  Speedup over number of processors
  data set remains constant
1
1

## Slide 10: Cache Coherency
Caches play key performance role
  reduce average data access time
  reduce bandwidth demands placed on shared interconnect and memory
But private processor caches create a problem
  copies of a variable can be present in multiple caches
  a write by one processor may not become visible to others
    they’ll keep accessing stale value in their caches
  cache coherence problem
  need to take actions to ensure visibility, preserve programmer intuition

## Slide 11: Ex: Cache Coherence Problem
L1 Cache
L1 Cache
L1 Cache
core0
core1
core2
MEMORY or L2
BUS
LD [100]
ST [100]
LD [100]
M[100]
D[100]
M[100]
?

## Slide 12: Snoopy Cache Coherence
Basic Idea
  Transactions on bus are visible to all processors
  Processors or their representatives can snoop (monitor) bus and take action on relevant events (e.g. change state)
  Implementing a “Protocol”
    Protocol is distributed algorithm: cooperating state machines
    set of states, state transition diagram, actions
Cache controller now receives inputs from both sides:
  requests from processor, bus requests/responses from snooper
  In either case, takes zero or more actions
    updates state, responds with data, generates new bus actions
Granularity of coherence is typically cache block
  like that of allocation in cache and transfer to/from cache

## Slide 13: Basic MSI Protocol
States
  Invalid (I)
  Shared (S): one or more
  Dirty or Modified (M): one only
Processor events:
  PrRd (read)
  PrWr (write)
Bus transactions
  BusRd: asks for copy with no intent to modify
  BusRdX: asks for copy with intent to modify
  BusWB: updates memory
Actions
  update state, perform bus transaction, flush value onto bus

## Slide 14: MSI State Diagram
S

## Slide 15: MSI Sample Coherence Messages
L1 Cache
L1 Cache
L1 Cache
core0
core1
core2
MEMORY or L2
BUS
LD [100]
ST [100]
LD [100]

## Slide 16: MESI
One extra state to reduce traffic. Check [sharers or no sharers]

## Slide 17: Next
Chip-level Multiprocessing (CMP)